## Slide 1: Dual-slope ADC

## Slide 2: Dual-slope ADC
The circuit consists of a high input impedance buffer A1, precision integrator A2 and a voltage comparator.
The converter first integrates the analog input signal Va for a fixed duration of 2n clock periods.
Then it integrates an internal reference voltage VR of opposite polarity until the integrator output is zero.

## Slide 3: Dual-slope ADC cont…
The number N of clock cycles required to return the integrator to zero is proportional to the value of Va averaged over the integration period.
N represents the desired output code.
Circuit Operation:
Before the START command arrives, the switch SW1 is connected to ground and SW2 is closed.
Any offset voltage present in the A1, A2, comparator loop after integration, appears across the capacitor CAZ tiIl the threshold of the comparator is achieved.
The capacitor CAZ thus provides automatic compensation for the input-offset voltages of all the three amplifiers.
Later, when SW2 opens, CAZ acts as a memory to hold the voltage required to keep the offset nulled.

## Slide 4: Dual-slope ADC cont…
At the arrival of the START, command at t = t1, the control logic opens SW2 and connects SW1, to Va and enables the counter starting from zero.
The circuit uses an n-stage ripple counter and therefore the counter resets to zero after counting 2n pulses.
The analog voltage Va is integrated for a frxed number 2n counts of clock pulses after which the counter resets to zero.
If the clock period is T, the integration takes place for a time T1 = 2n x T and the output is a ramp going downwards as shown in Fig.

## Slide 5: Dual-slope ADC cont…
The counter resets itself to zero at the end of the interval T1 and the switch SW1 is connected to the reference voltage (- VR).
The output voltage vo will now have a positive slope.
As long as vo is negative, the output of the comparator is positive and the control logic allows the clock pulse to be counted.
However, when vo becomes just zero at time t = t3, the control logic issues an end of conversion (EOC) command and no further clock pulses enter the counter.
It can be shown that the reading of the counter at t3 is proportional to the analog input voltage Va.

## Slide 6: Dual-slope ADC cont…
In Fig.
T1 = t 2 - t 1 = 2n counts / clock rate
t3 - t2 = digital count N / clock rate
For an integrator,
The voltage will be equal to at the instant t2 and can be written as

## Slide 7: Dual-slope ADC cont…
The voltage is also given by
So, Va (t2 - t1) = VR (t3 - t2)
Putting the values of (t2 –t1) = 2n and (t3 – t2) = N, we get
Va(2n) = (VR) N
Or, Va = (VR) (N/2n)

## Slide 8: Important Observations
Since VR and n are constant, the analog voltage Va is proportional to the count reading N and is independent of R, C and T.
The dual-slope ADC integrates the input signal for a fixed time, hence it provides excellent noise rejection of ac signals whose periods are integral multiples of the integration time T1. Thus ac noise superimposed on the input signal such as 50 Hz power line pick-up will be averaged during the input integration time. So choose clock period T, so that 2nT is an exact integral mu,ltiple of the line period (1/50) second = 20 ms.
The main disadvantage of the dual-slope ADC is the long conversion time. For instance, if 2n - T = 1/50 is used to reject line pick-up, the conversion time will be 20 ms.

## Slide 9: Uses
Dual-slope converters are particularly suitable for accurate measurement of slowly varying signals, such as thermocouples and weighing scales.
Dual-slope ADCs also form the basis of digital panel meters and multimeters.
Dual-slope converters are available in monolithic form and are available both in microprocessor compatible and in display oriented versions. The former provide the digital
code in binary form whereas the display oriented versions present the output code in a format suitable for the direct drive of LED displays.
The Datel Intersil ICL7109 is a monolithic 12-bit dual-slope ADC with microprocessor compatibility.

## Slide 10: Problems -1
A dual slope ADC uses a 16-bit counter and a 4 MHz clock rate. The maximum input voltage is +10 V. The maximum integrator output voltage should be - 8 V when the counter has cycled through 2n counts. The capacitor used in the integrator is 0.1 µF. Find the value of the resistor R of the integrator.
Solution:
Time period (t2 – t1) = 216 / 4 MHz = 65536/ 4 MHz = 16.38 ms
For the integrator
So, RC = -(10 V/ -8 V) 16.3 ms = 20.47 ms
R = 20.47 ms / 0.1 µF = 204.7 kΩ = 205 k Ω

## Slide 11: Problems -2
In the previous problem, If the analog signal Va is +4.129 V, 10.4, find the equivalent digital number.
Solution:
Since, Va = VR (N / 2n)
So the digital count N = 2n (Va / VR) = 65536 (4.129 V / 8 V) = 33825 for which the binary equivalent is 1000010000100001.