## Slide 1: Interrupt Programming with 8051

## Slide 2: Introduction to Interrupts
An interrupt is an external or internal event that interrupts the microcontroller to inform it that a device needs its service.
A set of program instructions written to service an interrupt is called the Interrupt Service Routine
8051 has six different sources of interrupts External: Power-up reset, INT0, INT1
Internal: Timer0, Timer1, Serial Port

## Slide 3: Interrupts vs Polling
There are two methods of writing software by which microcontroller can serve devices: Interrupts and Polling
Interrupt: whenever any device needs service, it notifies the 8051 by sending an interrupt signal
Polling: 8051 continuously monitors the status of a device, until some pre-determined condition is met, and then serves the device

## Slide 4: Interrupt
Microcontroller is free to execute any other programming task
Polling
Microcontroller cannot perform any task other than monitoring the device status
Which technique, interrupt or polling, avoids tying down the microcontroller?
Including reset, how many interrupts do we have in the 8051?

## Slide 5: Example of Polling
ORG 0H
MOV TMOD, #2
MOV TH0, #-10 SETB TR0
BACK:JNB TF0, BACK
CLR TR0 CLR TF0

## Slide 6: Interrupt Service Routine
When microcontroller receives an interrupt signal from any of the six interrupt sources it executes a call to interrupt service routine
For every interrupt, there must be an interrupt service routine
The interrupt service routine for every interrupt must be located at a fixed location in program memory, called interrupt vector.

## Slide 7: Interrupt Vector Table for 8051 Interrupts
Interrupt Source | ROM Location | Pin
Reset | 0000H | 9
INT0 | 0003H | 12(P3.2)
Timer0 | 000BH | 
INT1 | 0013H | 13(P3.3)
Timer1 | 001BH | 
Serial Port | 0023H | 

## Slide 8: Redirecting 8051 from Interrupt Vector Table at Power-Up
ORG 0H LJMP MAIN
MAIN:
ORG 30H
………….
…………. END
Bypass all the interrupt
vector locations

## Slide 9
Why do we put a LJMP instruction at address 0?
In the 8051, what memory area is assigned to a interrupt vector table?
The 8051 programmer cannot change the memory space assigned to interrupt vector table(T/F)
How many bytes of address space in the interrupt vector table is assigned to the timer 0 interrupt?
How many bytes of address space in the interrupt vector table is assigned to the reset interrupt, and why?
To put the entire Interrupt Service Routine in the space provided in interrupt vector table, it must be no more than bytes in size

## Slide 10: Enabling and Disabling Interrupt mechanism in 8051
Upon reset, all interrupts are disabled
The interrupts must be enabled by software, only then 8051 will respond to them
A register called IE( Interrupt Enable ) is responsible for enabling and disabling the interrupts
Upon reset, all bits of IE register are 0

## Slide 11: IE Register
ES ET1/ET0
EX1/EX0
-- -- ES ET1 EX1
0, Disables all interrupts
1, each interrupt is individually enabled or disabled by setting or clearing its enable bit.
enables or disables serial port interrupt enables or disables timer 1/0
interrupt
enables or disables external interrupt 1/0
D0
ET0 EX0
D7
EA
EA
 Write instructions to


enable serial interrupt and timer 0 interrupt Disable all interrupts

## Slide 12: How 8051 services an interrupt request ?
•
•
•
•
8051 finishes the instruction it is currently executing, and saves the contents of Program Counter on the stack (address of next instruction)
It jumps to the interrupt vector location corresponding to the interrupt source
Executes the interrupt service routine, until it encounters RETI instruction
Returns back to the place where it was interrupted, by popping the contents of stack on PC, and starts execution at that address

## Slide 14: A program to continuously read data from P0 and display it on P1 & simultaneously creating a square wave of 200us on P2.1 using timer 0.
ORG 0000H LJMP MAIN
;-- ISR for timer0 to generate square wave
ORG 000BH CPL P2.1 RETI
;--main program for initialization
ORG 0030H
MAIN:
;timer 0 in auto reload mode
BACK:
MOV TMOD, #2 MOV P0, #0FFH MOV TH0, #92H MOV IE, #82H SETB TR0 MOV A, P0 MOV P1, A SJMP BACK
END

## Slide 15: Programming Timer Interrupts
If timer interrupt bit in IE register is enabled, whenever the timer rolls over, TF flag is SET, and the 8051 is interrupted.
The interrupt service routine for timer can be placed at
  interrupt vector location if it is small enough, or
  elsewhere by using proper redirection at interrupt vector location

## Slide 16: Programming External Hardware Interrupts
8051 has the following external interrupts
  RESET
  INT0
  INT1
RESET is used for power-on reset
Therefore there are two external interrupts INT0 & INT1, that can be used by external hardware(devices) to interrupt 8051

## Slide 17: How interrupts are activated?
There are two activation levels for the external hardware interrupts
  Level triggered
  Edge triggered
Level triggered interrupts is the default mode upon RESET of the 8051

## Slide 18: Level Triggered Interrupt
Vcc
P1.3
INT0 and INT1 are normally held high
If a low-level signal is applied to them, it triggers the interrupt
Vcc
INT0
LED

## Slide 19: How 8051 knows that an interrupt is activated?
P1.3
Vcc
INT0
LED
Device
Normally High
Interrupt Activated
If the hardware interrupts are enabled in the IE register,8051 samples the INT 0/1 pin for a low level signal once each machine cycle.
If during sampling 8051 senses the signal on INT0/1 to be low, the interrupt is activated

## Slide 20: What is the minimum duration for which INT 0/1 pin must be held low for interrupt to be activated?
The pin must be held low until the start of the execution of Interrupt Service Routine
The minimum duration is 4 machine cycles.
How can we make sure that a single interrupt is not interpreted as multiple interrupts?

The low-level on INT0/1 pin be brought back to high before the execution of RETI instruction in Interrupt Service Routine

## Slide 21: Remember that…..
There are two activation levels for the external hardware interrupts
  Level triggered
  Edge triggered
Level triggered interrupts is the default mode upon RESET of the 8051

## Slide 22: Edge Triggered Interrupts
•
•
We must program the bits of TCON register to make interrupts edge-triggered
When a high-to-low signal is applied to INT0/1 pin, the 8051 will be interrupted
P1.3
Vcc
INT0
LED
Device
High-to-low transition

## Slide 23: Role of TCON Register
IT0
IE0
IT1
IE1
TR0
TF0
TR1
TF1
D0
D7
TCON.0
TCON.2
0, INT0 becomes level-triggered interrupt 1, INT0 becomes edge-triggered interrupt
0, INT1 becomes level-triggered interrupt 1, INT1 becomes edge-triggered interrupt
To make INT0 edge-triggered the instruction is SETB TCON.0
To make INT1 edge-triggered the instruction is SETB TCON.2

## Slide 24: How Edge-triggered Interrupts are activated and serviced by 8051?
The falling edge on INT0/1 pins is latched by 8051, and held by the TCON register
TCON.1(IE0) AND TCON.3(IE1) bits are used by 8051 to keep track of edge-triggered interrupts only
When edge(high-to-low) transition takes place on INT0/1 pin, 8051 does the following-
  Sets high IE0/1 bit in the TCON register
  Jumps to the interrupt vector location
  Executes the interrupt service routine
to be continued…

## Slide 25: Role of TCON Register
IT0
IE0
IT1
IE1
TR0
TF0
TR1
TF1
D0
D7
TCON.1
TCON.3
Set by CPU when external interrupt edge on INT0 pin is detected
Set by CPU when external interrupt edge on INT1 pin is detected
IE0/1 are also called Interrupt-in-service flags
When set to 1, indicates 8051 is executing an interrupt service routine

## Slide 26
At the end of service routine, RETI instruction is executed
– This clears the IE0/1 interrupt-in-service flag
What is the role of RETI instruction…
In edge-triggered interrupts
Timer interrupts
Can we use RET instruction in Interrupt service routine?

## Slide 27: Programming Serial Communication Interrupts

## Slide 28: Serial Communication using Polling
A program to transfer character ‘A’ serially at 4800 baud, continuously
ORG 0H
MOV TMOD, #20H MOV TH1, #-6 MOV SCON, #50H SETB TR1
;timer 1, mode 2
;set baud rate to 4800
;serial mode 1
;start timer 1
AGAIN: MOV SBUF, #’A’ ;send character ‘A’ for
;transmission
HERE: JNB TI, HERE ;wait until TI flag is set
CLR TI ;clear TI to transmit next char SJMP AGAIN

## Slide 29: Serial Communication Interrupt Flags
SM0 | SM1 | SM2 | REN | TB8 | RB8 | TI | RI
SCON
Register
TI(Transmit Interrupt): is raised when last bit, i.e. the stop bit, is transferred
RI(Receive Interrupt): is raised when the entire frame of data, including the stop bit is received
In polling method, 8051 just waits for the TI or RI flag to be raised, does nothing else

## Slide 30: Using Serial Interrupt with 8051
In 8051 there is only one interrupt for both serial data transmission and reception
When TI or RI is raised by serial data transfer, 8051 is interrupted, and jumps to interrupt vector location 0023H to execute the interrupt service routine(ISR)
In ISR, 8051 must examine TI and RI flags to determine which one caused the interrupt

## Slide 31
A program to
continuously read data from P1 and send it to P2
receive data from serial port and send it to P0
 | ORG 0H LJMP MAIN ORG 0023H LJMP SERIAL | ORG 100H SERIAL: JB TI, TRANS MOV A, SBUF MOV P0, A CLR RI RETI
MAIN: | MOV P1, #0FFH MOV TMOD, #20H MOV TH1, #0FDH MOV SCON, #050H MOV IE, #10010000B SETB TR1 | TRANS: CLR TI RETI END
BACK: | MOV A, P1 MOV P2, A SJMP BACK | 

## Slide 32: Interrupt Priority in 8051
What happens if two interrupts are activated at the same time?
Which of these two interrupts is serviced first?
The interrupt which has the highest priority is serviced first
By default, 8051 assigns a priority level to all interrupts upon RESET

## Slide 33: 8051 Interrupt Priority upon RESET
Highest to Lowest Priority
External Interrupt 0 INT0
Timer Interrupt 0 TF0
External Interrupt 1 INT1
Timer Interrupt 1 TF1 Serial Communication RI + TI

## Slide 34: What happens if interrupts INT0, TF0, INT1 are activated at the same time? Assume default priority levels and edge-triggered external interrupts.
They are latched and kept internally by 8051
Then 8051 polls all interrupts according to the default priority levels
If any interrupt is activated, it is serviced in that sequence.
Therefore IE0(INT0) is serviced first, then TF0(timer0), and finally IE1(INT1)

## Slide 35: Interrupt Priority Register
PS PT1 PX1 PT0 PX0
Serial Port Priority bit Timer1 interrupt priority bit
External interrupt 1 priority bit Timer0 interrupt priority bit External interrupt 0 priority bit
-- | -- | PT2 | PS | PT1 | PX1 | PT0 | PX0
IP
Register
D7 D0
Priority bit = 1, assigns high priority
0, assigns low priority

## Slide 36
Assume that after RESET, the Interrupt priority is set by the instruction
MOV IP, 00001100B
Discuss the sequence in which the interrupts are serviced.
What happens if the 8051 is executing the ISR of an interrupt and another higher priority interrupt is activated?
Upon RESET all interrupts have the same priority.(T/F)