## Slide 1: Sequential PLDs
by
Manikandan AVM
Assistant Professor, ECE, SRMIST, KTR

## Slide 2: Sequential Programmable Devices
The combinational PLD consist only gates
Sequential Programmable Devices includes both gates and filp-flop
Type of sequential Programmable Devices:
  Sequential (simple) programmable logic device (SPLD)
    Field-programmable logic sequence (FPLS, defunct – too hard to use)
    Registered PAL / macrocell structure
  Complex programmable logic device (CPLD)
    Collection of SPLDs on a chip
  Field programmable gate array (FPGA)
    Logic blocks (look-up tables, multiplexers, gates, flip-flops)
    Programmable input/output blocks
    Programmable interconnections

## Slide 3: SPLD
SPLD: consist PAL and D flip-flop
Each section in SPLD is called Microcell
The basic microcell logic
  AND-OR array
  Edge-triggered D flip-flop
  Three-state buffer(inverter)
A typical SPLD has from 8 to 10 macrocells within one IC package

## Slide 4
The AND-OR array is exactly the same as the one found in the combinational PLD.
However, it has edge-triggered flip-flops between the AND-OR array and its outputs.
All of the flip-flops are connected to a common clock input CLK, and change state on the rising edge of the clock.
Each flip-flop drives an output pin through a 3- state buffer; the buffers have a common output-enable signal, OE_L.
Notice that the registered output pins contain the complement of the signal produced by the AND-OR array.
The connection from the D flip-flop outputs into the AND-OR array makes it easy to design shift registers, counters, and general state machines.
D flip-flop outputs are available to the AND-OR array whether or not the output three-state drivers are enabled. Thus, the internal flip-flops can go to a next state that is a function of the current state even when the outputs are disabled.

## Slide 5
16R8 –sequential logic PAL
8 inputs, each with true & complement
8 outputs, each with
  D flip-flop With feedback for FSMs
  8 product terms that can AND any of:
    8 inputs or their complements
    8 feedbacks or their complements from D flip-flops
One clock for all FFs
One tri-state control for all outputs